Introduction to digital control
In class activities
Ranjeet Utikar
2023-10-08
# 1. Activities
Given Transform :
find .
Solution
First find the time domain function .
1. Inverse Laplace Transform :
  The inverse Laplace transform of will give the time-domain function . We can use partial fraction decomposition to find it:
  Solving for and :
  Setting :
  Setting :
  Therefore,
2. Inverse Laplace Transform in Time-Domain :
Using standard Laplace transform pairs:

Sampling the Function :
We are interested in finding , which implies evaluating the limit of at discrete points :

Taking the Limit :

Since , as , .
Therefore, the limit becomes:

z-transform:
Sample at intervals of .

The z-transform of a discrete-time sequence is given by:

Substitute the expression for :

Separate the summation:

Each summation is a geometric series:
For the first summation:

For the second summation:

Consider the transfer function below
The zero hold transfer function is given by

determine the discrete transfer function using c2d command for different Ts. Plot the responses.
Solution
The code is given in mlx file.
Consider a continuous process

convert G(s) to discrete transfer function and plot the step response. Try different hold functions.
Solution
The code is given in mlx file.
For the transfer function

plot the effect of sample time on response.
Solution
The code is given in mlx file.
Design a feedback control system around the first-order plant

with the requirements that
1. the steady-state error is maximum 2% for a ramp input and
2. the phase margin is greater than 48 degrees.
Use controller transfer function and check phase margin.

Solution
To design a feedback control system for the first-order plant:
Steady-State Error for a Ramp Input
The system’s steady-state error for a ramp input is determined by the type and the system gain . A unity feedback system with a proportional controller can be considered:
The type of system is determined by the number of poles at the origin (s=0). This system is Type 0 because there is no pole at the origin in G(s).
, the velocity error constant is given by:

The steady-state error for a ramp input is:

To satisfy , .
Given , if we use a proportional controller with gain :

To achieve :

Hence, the proportional gain must be greater than 10.
- P only controller mlx file.
- PI controller mlx file.
1. Convert the controller from Equation 6 to discrete form using different sample times. Plot the Bode plot for the continuous and discrete controller and discuss the differences.
2. Design and compare continous and digital controller for the following transfer function